## Slide 1: Solar
Ribby, Sophie

## Slide 2: Contents
- Solar energy
- History
- Technologies
- Solar power
- Types of solar energy technologies
- PVS
- STE
- thermal
- electricity
- The future of solar energy
Notes: http://www.rpi.edu/dept/phys/Courses/PHYS1010/Fall07/Persans.pdf
http://www.physics.ohio-state.edu/~wilkins/energy/Companion/E21.4.pdf.xpdf
http://science.nasa.gov/science-news/science-at-nasa/2002/solarcells/
http://www.physlink.com/Education/AskExperts/ae451.cfm
http://science.howstuffworks.com/environmental/energy/solar-cell.htm
http://environment.nationalgeographic.com/environment/global-warming/solar-power-profile/
http://southwest.mpls.k12.mn.us/uploads/solar_and_hydroelectric_power.pdf

## Slide 3: What is solar energy?
Radiant light and heat from the sun!
Notes: Electromagnetic waves and photon particles flying through spaces' vacuum to Earth

## Slide 4: History of solar energy
1839: Edmund Becquerel discovers the photovoltaic effect (discovers that electric current is created when a material is exposed to light)
1905: Albert Einstein formulates the photon theory of light which describes how light can 'liberate' electrons on a metal surface
1918: Jan Czochralski figures a method to grow single-crystal silicon which laid the foundations for solar cells based on silicon
1954L David Chapin, Calvin Fuller, Gerald Pearson of Bell Labs are credited with the world's first photovoltaic cells (solar cells) -> made the first device to convert sunlight to electrical power
Notes: Some of these events we have chosen from a short but rich history of solar energy may not seem significant but as we explain some of the vocabulary involved, such as what the photovoltaic is and solar cells are, you will realize why these events were picked as significant.

## Slide 5
Solar technology can be classified as ACTIVE or PASSIVE depending on the way it is captured, converted, and distributed.
1) Active: converts solar energy into usually heat or electrical energy; uses electrical or mechanical equipment for this conversion
2) Passive: relies on inherent thermo-dynamic properties of the system or materials to operate; no external energy sources
Notes: Active:
Benefits: controls (electrical) to maximize effectiveness
ex) a passive solar thermal array which does not rely on pumps and sensors will only start circulating when a certain amount of internal energy has built up in the system. Using sensors and pumps, a relatively small amount of energy (i.e. that used to power a pump and controller) can harvest a far larger amount of available thermal energy.
Downside: external power sources may fail, controls need maintenance

## Slide 6: Solar power
: the conversion of sunlight into electricity
-> directly: photovoltaics (PV) -> photovoltaic effect (PVE)
-> indirectly: concentrated solar power (CSP) -> use of mirrors or lenses to concentrate a large area of sunlight (STE: solar thermal energy)
Notes: Direct collector systems are best applied in climates that have large amounts of sun. Indirect collector systems are best applied in cooler climates because heat transfer fluids such as hydrocarbons or refrigerants have lower freezing temperatures than water.
A solar photovoltaic power plant converts sunlight into direct current electricity using the photoelectric effect. Inverters change the direct current into alternating current for connection to the electrical grid. This type of plant does not use rotating machines for energy conversion.
Solar thermal power plants are another type of solar power plant. They use either parabolic troughs or heliostats to direct sunlight onto a pipe containing a heat transfer fluid, such as oil. The heated oil is then used to boil water into steam, which turns a turbine that drives an electrical generator. The central tower type of solar thermal power plant uses hundreds or thousands of mirrors, depending on size, to direct sunlight onto a receiver on top of a tower. Again, the heat is used to produce steam to turn turbines that drive electrical generators.
The two main technologies used to convert solar energy are photovoltaic cells (PV) and solar thermal systems.

## Slide 7: 1. Photovoltaic system
- uses solar panels to convert sunlight into electricity
- efficiency of commercial PV is in the range of 12-20%
- semiconductor
Notes: 12-20% (higher efficiencies are being developed) - depends on the semiconductor used
semiconductor- a material which has electrical conductivity between that of a conductor such as copper and an insulator such as glass.

## Slide 8
Notes: The 4 basic components of a solar photovoltaic power plant: Solar cells turn sunlight into direct current electrical energy. A cable or bus network transfers the DC power to a centralized inverter. That inverter changes the power from direct current to alternating current. And, transformers step up the voltage to match the supply grid and output the generated power. It is different from other green energy technologies because there is no mechanical process involved in producing the electricity.

## Slide 9: Types of semi conductors used
crystalline silicon solar cells
- monocrystalline
- polycrystalline
thin film solar cells
- amorphous silicon
- CIGS (copper indium gallium selenide), GdTe-CdS
organic solar cells
Notes: semiconductor solar cells:
- crystalline silicon solar cells: monocrystalline, polycrystalline -> 14-20%, long life
- thin film solar cells:
- amorphous silicon thin-film silicon solar cells: much less expensive than crystalline, efficiency 6-10%
- CIGS (copper indium gallium selenide), CdTe-CdS thin film: efficiency 10%, very high absorption coefficient -> amount of materials required is small and the production process is simpler -> unit price per peak watt is lower than crystalline silicon solar cells
- organic solar cells have low efficiency and a short lifetime -> market share is insignificant
Centre for Alternative Technology (UK)
PV panel power output decreases by less than 1% per year. Panels do experience a significant amount of physical decay (yellowing, laminate peeling off) if they are exposed to the elements for 10 or 20 years, but the effect on their performance is limited. This suggests a PV installation should produce electricity for 30 years or longer.
To increase efficiency: Concentrated photovoltaics (CPV) may reduce cost by concentrating up to 1,000 suns (through magnifying lens) onto a smaller sized photovoltaic cell. However, such concentrated solar power requires sophisticated heat sink designs, otherwise the photovoltaic cell overheats, which reduces its efficiency and life. To further exacerbate the concentrated cooling design, the heat sink must be passive, otherwise the power required for active cooling with reduce the overall efficiency and economy.

## Slide 10
Notes: how it works:
- composed of semi conductors such as silicon
- the semiconductor materials are specifically arranged in two layers between positive and negative electrodes
- one layer: n-type semiconductor (negative)- modified to have an excess of electrons
- other layer: p-type semiconductor (positive)- modified to have an excess of electron “holes”
- at the junction of the two layers the electrons of the n-type semiconductor are inclined to cross over to the p-type layer to fill the electron vacancies
- as the electrons and holes combine an equilibrium is reached whereby a fixed electric field is created at the P-N junction
- when photons of light of a particular wavelength strike the solar cell, photovoltaic effect (the creation of voltage or electric current in a material upon exposure to light) causes electrons in the cell to be mobilized
- the field gradient of the electric field (the rate of change of the electric field at an atomic nucleus generated by the electronic charge distribution and the other nuclei) allows electrons to pass through the fixed field to the n-type layer but not to return in the opposite direction
- the charge imbalance between the layers leads to the electrons travelling out of the n-type semiconductor into the metal electrodes on the surface of the cell

## Slide 11: Problem!
The typical energy of photons in the visible spectrum is 2 eV. Explain why a semiconductor with an energy gap between the valence and conduction bands of more than 2 eV would not be suitable in a photovoltaic cell.
E (cb) - E (vb)
= h*V (Planck's constant*voltage) (eV)
Notes: The energy of the photons excite the electrons in the valence (outermost shell) band to the conduction band (electron level to transmit electricity). However, if the energy does not match the gap of the bands, it would ‘overshoot’ or ‘undershoot’ and not be able to produce electricity. Therefore, the semiconductor requires a certain range (gap) for the photon to hit, which in this case is 2eV.

## Slide 12: 2. Solar thermal energy
- converts sunlight (solar radiation) to thermal energy (heat)
- solar thermal collectors classified as:
- low-
- medium-
- high- temperature
Notes: - low: heats swimming pools
- medium: usually flat plates, residential and commercial use
- high: concentrate sunlight using mirrors or lenses and are generally used for electric power production
- connected to Solar power plants that usually use the more complex collectors to generate electricity by heating water to produce steam which drives a turbine, engine, pump cycles connected to an electrical generator
- more efficient that photovoltaics

## Slide 13: Types of collectors
- solar water heating
Notes: - Solar Water Heating:
- The simplest form is to allow sunlight to shine on an exposed water tank. Painting the tank a dark colour reduced reflectivity, and consequently increases absorption. The primary disadvantage of this system, is that it is equally good at radiating heat, and thus cools quickly overnight.
The next simplest form of solar collector is the black pipe collector. The most common configuration is to use black polypropylene pipes laid out to collect solar radiation. Commonly used for solar pool heating systems, black pipes are laid out on a north-facing roof surface. A pump is used to circulate water, and is set to operate only while the sun shines.
The limitation of the pipe collector is that since black surfaces are also effective radiators of infra-red radiation (heat), the effective efficiency falls, as the temperature of the water approaches the ambient temperature, as heat is lost by radiation, and direct convection to the surrounding air; limiting the practical temperature to about 60˚C.

## Slide 14
- flat plate collector
Notes: flat plate collector
(1) a dark flat-plate absorber of solar energy
(2) a transparent cover that allows solar energy to pass through but reduces heat losses
(3) a heat-transport fluid (air, antifreeze or water) to remove heat from the absorber
(4) a heat insulating backing
The absorber consists of a thin absorber sheet (of thermally stable polymers, aluminum, steel or copper, to which a matte Sunlight passes through the glazing and strikes the absorber plate, which heats up, changing solar energy into heat energy. The heat is transferred to liquid passing through pipes attached to the absorber plate. Absorber plates are commonly painted with "selective coatings," which absorb and retain heat better than ordinary black paint. Absorber plates are usually made of metal—typically copper or aluminum—because the metal is a good heat conductor. Copper is more expensive, but is a better conductor and less prone to corrosion than aluminum.
In water heat panels, fluid is usually circulated through tubing to transfer heat from the absorber to an insulated water tank. This may be achieved directly or through a heat exchanger. Most air heat fabricators and some water heat manufacturers have a completely flooded absorber consisting of two sheets of metal which the fluid passes between. Because the heat exchange area is greater they may be marginally more efficient than traditional absorbers.

## Slide 15
- evacuated tube collector
Notes: Evacuated heat pipe tubes are composed of multiple evacuated glass tubes each containing an absorber plate fused to a heat pipe. The heat from the hot end of the heat pipes is transferred to the transfer fluid (water or an antifreeze mix) of a domestic hot water space heating system in a heat exchanger called a "manifold". The manifold is wrapped in insulation and covered by a sheet metal or plastic case to protect it from the elements.
The vacuum that surrounds the outside of the tube greatly reduces convection and conduction heat loss to the outside, therefore achieving greater efficiency than flat-plate collectors, especially in colder conditions. This advantage is largely lost in warmer climates, except in those cases where very hot water is desirable, for example commercial process water. The high temperatures that can occur may require special system design to prevent overheating.

## Slide 16: Efficiency
- different forms of collectors are appropriate at different temperatures
- higher temperature -> plant uses higher-temperature dry heat exchangers -> less water use -> GOOD!
- higher temperature -> heat storage more efficient (more watt-hours are stored per unit of fluid)
- very high temperatures -> difficult.
Notes: As the temperature increases, different forms of conversion become practical. Up to 600 °C, steam turbines, standard technology, have an efficiency up to 41%. Above 600 °C, gas turbines can be more efficient. Higher temperatures are problematic because different materials and techniques are needed. One proposal for very high temperatures is to use liquid fluoride salts operating between 700 °C to 800 °C, using multi-stage turbine systems to achieve 50% or more thermal efficiencies.[28] The higher operating temperatures permit the plant to use higher-temperature dry heat exchangers for its thermal exhaust, reducing the plant's water use – critical in the deserts where large solar plants are practical. High temperatures also make heat storage more efficient, because more watt-hours are stored per unit of fluid.
Advantages
Very high temperatures reached. High temperatures are suitable for electricity generation using conventional methods like steam turbine or a direct high temperature chemical reaction such as liquid salt.[15]
Good efficiency. By concentrating sunlight current systems can get better efficiency than simple solar cells.
A larger area can be covered by using relatively inexpensive mirrors rather than using expensive solar cells.
Concentrated light can be redirected to a suitable location via optical fiber cable for such uses as illuminating buildings.
Heat storage for power production during cloudy and overnight conditions can be accomplished, often by underground tank storage of heated fluids. Molten salts have been used to good effect.
Disadvantages
Concentrating systems require sun tracking to maintain Sunlight focus at the collector.
Inability to provide power in diffused light conditions. Solar Cells are able to provide some output even if the sky becomes a little bit cloudy, but power output from concentrating systems drop drastically in cloudy conditions as diffused light cannot be concentrated passively.

## Slide 17: Solar architecture
- the integration of solar panel technology with modern building techniques
Notes: Another solar energy technology.
Windows, walls, and floors are made to collect, store, and distribute solar energy in the form of heat in the winter and reject solar heat in the summer

## Slide 18: Difference between photovoltaic cell and solar panel
- direct
- converts to electricity
- lower efficiency
(upto 24%)
- does not use machines for energy conversion
- indirect
- converts to thermal energy (heat)
- higher efficiency (upt0 50%)
- uses rotating machines to convert thermal energy to electricity

## Slide 19: The future of solar energy
average solar power density of the radiation: 1366 Wm-2 (the solar constant)
Notes: before we conclude our presentation, let us tell you some facts about the sun.
the average power density of solar radiation just outside the atmosphere of the Earth is 1366 W/m2, widely known as the solar constant
- The definition of the meter is one over 10,000,000 of Earth’s meridian, from the North Pole to the equator, see Fig. 1.1. This definition is still pretty accurate according to modern measurements. Therefore, the radius of Earth is (2/π) × 107 m.

## Slide 20
Notes: The total power of solar radiation reaching Earth is then
Solar power = 1366 × 4 × 1014 ∼= 1.73 × 1017 W. (1.1) π
Each day has 86,400 s, and on average, each year has 365.2422 days. The total energy of solar radiation reaching Earth per year is
Annual solar energy = 1.73 × 1017 × 86400 × 365.2422 ∼= 5.46 × 1024 J. (1.2)
Or 5,460,000 EJ/year.

## Slide 21: the future.................................
Notes: For the solution for Global Warming, we really do need to find an alternative energy source other than the coal industries which produce CO2 that contribute a lot to the enhanced greenhouse effect.
Solar Power Energy is based on a renewable resource, never depletable unless the explosion of the Sun happens. Like wind power, using a resource available from nature avoids our sole reliance on mineral resources (coal, oil) which may completely disappear at the speed of earth’s consumption. It will optimally preserve its resources as it is now as a non-pollutive further developing efficient method.
Not all solar radiation falls on Earth’s atmosphere reaches the ground. About 30% of solar radiation is reflected into space. About 20% of solar radiation is absorbed by clouds and molecules in the air. About three quarters of the surface of Earth is water. However, even if only 10% of total solar radiation is utilizable, 0.1% of it can power the entire world.
A solar building. As the venue of the 2010 International Solar City Congress, Himin Solar Energy Group designed and built this 75,000-m2 (800,000-ft.2) building in D ́ezh ̄ou, Sh ̄and ̄ong province, China, with more than 60% of energy supplied by solar devices.

## Slide 22: Citation
http://www.rpi.edu/dept/phys/Courses/PHYS1010/Fall07/Persans.pdf
http://www.physics.ohio-state.edu/~wilkins/energy/Companion/E21.4.pdf.xpdf
http://science.nasa.gov/science-news/science-at-nasa/2002/solarcells/
http://www.physlink.com/Education/AskExperts/ae451.cfm
http://science.howstuffworks.com/environmental/energy/solar-cell.htm
http://environment.nationalgeographic.com/environment/global-warming/solar-power-profile/
http://southwest.mpls.k12.mn.us/uploads/solar_and_hydroelectric_power.pdf
Physics of Solar Energy - C. Julian Chen
Department of Applied Physics and Applied Mathematics
Columbia University
- info and pictures